## Slide 1: ALD Process for Top-Gating 2D Materials
Project Members: Akash Levy, Jung-Soo Ko
Mentor: Michelle Rincon
ENGR241 Project Proposal

## Slide 2: Motivation
  Many research groups are studying 2D materials at Stanford
    Poplab (EE)
    Evan Reed group (MATSCI)
    Saraswat group (EE)
    More…
  For 2D FET devices, ALD is needed to produce high-quality gate dielectrics for CMOS integration
  Process flow involves metal buffer layer for adhesion and other tricks that are not currently documented anywhere for SNF members
  No optimization of the processes for high-quality TMD gate dielectrics

## Slide 3: Aim & Goals
  To develop and document process flow for ALD top-gating on transition metal dichalchogenides (TMDs), e.g. MoS2, WSe2
  Aiming for reliable and controlled growth of high-k materials
  Optimization of process parameters/conditions for best film quality/electrical properties
  Will make data available to lab members via wiki page
Process Flow Development
Parameter Optimization
Comprehensive Documentation
SNF Database

## Slide 4: Process Flow
  Start with MoS2 thin film wafers (pre-grown outside SNF)
  Perform e-beam evaporation to deposit metal buffer layer
  ALD for high-k gate oxide
  Perform e-beam evaporation for metal top-gate contact
  Patterning via photolithography (test structure masks already made)
Process Flow
Diagram
(Jung-Soo)
Here!!! TODO

## Slide 5: Parameters to Optimize
  TMD material: will probably just use MoS2 this quarter
  High-k material: alumina, hafnia, zirconia
  Buffer layer sizing: can probably filter this a lot with initial testing
  Pulse strength: can greatly affect thin film quality if not adjusted properly
  Anneal/growth temperature: RT, 250C, 300C, 350C
  Plasma vs. thermal
  Purge time: what purge time is sufficient?
  Anything missing?
  Still need to determine exact wafer splits…
    Will be based on initial testing and feedback from people in Poplab with tribal knowledge of the currently-used recipe
    What is a reasonable number of wafers to expect to run?

## Slide 6: Characterization
  All the typical MOSFET characterizations
    I-V curves
    C-V curves
    Gate breakdown voltages
  Imaging
    AFM images for surface roughness
    SEM images
  Will use micromanipulator for characterization (which Akash is trained on)
  Imaging will be done with help of Jung-Soo’s colleagues
  Will use Fiji3 for ALD experiments since it should produce best quality high-k dielectric films

## Slide 7: Tentative Timeline
Week | Description of Activities
2 | Jung-Soo: finishing up lab membership training Akash: tool shadowing/training for Fiji, AJA, spectrometry
3 | Both: tool shadowing/training for AFM, SEM, Fiji, AJA, spectrometry
4 | Both: tool shadowing/training for AFM, SEM, Fiji, AJA, spectrometry
5 | Finish up training, run initial experiments to determine wafer splits
6 | ALD/e-beam deposition under various settings
7 | Photolithographic patterning of microstructures
8 | Electrical characterization and imaging
9 | Adjust and continue
10 | Wrap up, documentation, database compilation, planning for next quarter

## Slide 8: Training Required
  Akash is a lab member and is qualified (through EE 312) on:
    All photolithography equipment
    Wet benches
    Furnaces
    Micromanipulator6000
  Jung-Soo will be a new lab member
  Both Akash and Jung-Soo need training on:
    ALD equipment (Fiji)
    E-beam evaporation (AJA)
    AFM
    SEM

## Slide 9: Tentative Budget (TODO: finish Jung-Soo)
Equipment Name | Training (?) | Usage (?)
Fiji | 3h(train) + n hours | $80X3X2 + $50Xn
SEM |  | 
AFM |  | 
Si wafers | N wafers | $14XN
AJA e-beam | 1h(train) + n hours | $80
furnace |  | 
headway | N hours | $10
Laurell | N hours | $10
Wet bench | N hours | $10
YES oven | N hours | $35
Heidelberg | N hours | $35
NIR Spectrometer | Need training | $20
Micromist Coater | No training | $10

## Slide 10: Recap of Deliverables
  Wiki page on optimized process flow for top-gating 2D materials
    Best conditions for each top-gate material will be specified
    Recipes will be made available to lab members on the equipment
  Electrical characterization data (raw and summarized) will be made available to lab members via database
    I-V curves
    C-V curves
    Gate breakdown voltage
  All imaging data taken will be made available to lab members in raw and summarized form
    AFM
    SEM

## Slide 11: Thank you!
Questions?